FRAME BUFFER
PRIYANKA & MOHAN

---
CONTENTS
Display Devices
Frame Buffer
Frame Buffer Device (fbdev)

---
  DISPLAY
Display is a term used to describe the device used to view images
and text.
Some of the important display devices:
Cathode Ray Tube Display
Liquid Crystal Display

---
  CRT DISPLAY DEVICE

---
CRT DISPLAY Cont..
Cathode Ray Tube consist of :
      a. Electron gun
      b. Heater
      c. Cathode
      d. Control grid
      e. Pre – accelerating anode
       f. Focusing anode
      g. Electrostatic deflection plates
      h. Fluorescent screen

---
 CRT DISPLAY Cont..
Applications of CRT:
       In TVs , radar systems and CRO we are using CRT principle.
Advantages:
       We can easily increase the brightness by reflecting the light.
       Low cost as compared to LCD and plasma.
       The quality of image displayed is higher to the LCD and plasma.

---
 CRT DISPLAY Cont..
Disadvantages:
      CRT emits small amount of x-ray radiations which causes health
       hazard.
      CRT operates at high voltage which can overheat system and
       results in an implosion.

---
 CRT COLOUR MONITORS
  Color monitors use a combination of phosphors that emits different
   colored light.
  We have two types of technologies:
    1. Beam penetration method
    2. Shadow mask method

---
 BEAM PENETRATION METHOD
Applications:
      Used in Random scan system.
Advantages:
      Less expensive.
Disadvantages:
     Quality of image are not good compared to other methods.
     Four colors are allowed only.

---
 SHADOW MASK METHOD

---
 LCD DISPLAY DEVICE
LCD structure

---
 LCD DISPLAY Cont..

---
 LCD DISPLAY DEVICE cont..
Orientation of molecules-LCD
Liquid crystal phases

---
 LCD DISPLAY Cont..
We have two types of LCD displays:
    1.transmissive
    2.reflective
Transmissive display

---
  LCD DISPLAY Cont..
Reflective display

---
  LCD DISPLAY Cont..
Advantages:
   LCD consumes less power compared to CRT and LED.
   LCD is low cost ,thinner and lighter compared to CRT and LED.
Disadvantages:
   Low reliability.
   More light sources are used.
   Speed is very low.
Applications:
   Computers ,clocks ,science and medical equipments ,mobiles etc.,

---
LCD DISPLAYS

---
SUB-SYSTEMS
How to display things in the Linux world?
Different solutions, provided by different subsystems:
       FBDEV: Frame buffer Device
       DRM/KMS: Direct Rendering Manager / Kernel Mode Setting
       V4L2: Video For Linux 2

---
FRAME BUFFER
Frame buffer is a computer memory
organized into an m x n rectangular grid of dots, called picture elements (or) pixels.
Its a part of GPU memory(VRAM).

---
FRAME BUFFER
Holds the pixel properties.
No. of bits per pixel (depth).
Performance of the graphics depends above properties.
Picture Quality
Brightness

---
FRAME BUFFER
Bitmaps
Bits per pixel
1 bit /pixel = 2 colors
2 bits/pixel = 4 colors
4 bits/pixel = 16 colors
8 bits/pixel = 256 colors

---
FRAME BUFFER
Size of frame buffer ?
Color depth
Resolution
Size of FB = M x N x P.
   M : no. of horizontal scan lines.
   N : no. of pixels per scan lines.
   P : no. of bits per pixel.
cat /sys/class/graphics/fb0/virtual_size

---
FRAME BUFFER
How FB communicate with Standard display ?
The video RAM is continuously read out by a specialized DMA component on the video card and sent to the monitor.

---
FRAME BUFFER

---
FRAME BUFFER
Double buffering
double buffering can be used to show one image or frame while a separate frame is being buffered to be shown next.
This method makes animations and games look more realistic than the same done in a single buffer mode

---
GPUs
Graphics Processing Unit
A Graphics Processing Unit (GPU) is a single-chip processor primarily used to manage and boost the performance of video and graphics.
Need of separate processor ?
Faster execution.
More ALUs compared to CPU.

---
GPUs

---
FBDEV
The frame buffer device provides an abstraction for the graphics hardware.
/dev/fb0 is actual frame buffer device node.This node has a unique access to the devices based on major and minor numbers.
drivers/video/fbdev/ contains the drivers for the video.

---
Driver Vs Device
 Driver
 Device
fbdev
Frame buffer
dmesg
BCM2708FB: allocated DMA memory %08x

---
Flow Of Drivers
 Device or
end point
Terminologies
 PCI,PnP,interrupt controller,
CPU,interrupt handler,
 Driver