ABS (android boot sequence)
MOHAN

---
CONTENTS
UBOOT & UEFI & POST
BASIC KERNEL
DTS & DTSI
ANDROID BOOTING SEQUENCE

---
POST
* When we press the power button, the Boot ROM code starts executing from a pre-defined location which is hardwired in ROM(firmware code specific to individual devices)
* It loads the Boot loader into RAM and starts executing with the help of UEFI.

---
uboot
Boot loader :
* It is a vendor-proprietary image responsible for bringing up the kernel on a device.
* It provides the basic infrastructure to bring up a board to a point where it can load a Linux kernel and start booting your operating system.
entry point,load address etc...
* U-Boot is both a first-stage and second-stage bootloader.
* It is loaded by the system's ROM or BIOS from a supported boot device, such as an SD card, SATA drive, NOR flash (e.g. using SPI or I²C), or NAND flash.
* U-Boot has support for USB, so it can use a USB keyboard to operate the console

---
UEFI
UEFI:
The Unified Extensible Firmware Interface is a specification that defines a software interface between an operating system and platform firmware.
UEFI is expected to eventually replace BIOS. Like BIOS, UEFI is installed at the time of manufacturing and is the first program that runs when a computer is turned on.

---
Uboot & UEFI
Primary boot interface (eMMC)
|
PBL,start
elf_loader_entry, Start
PBL, End
|
SBL1, Start
PMIC Image Loaded, Delta
Bootup frequency set to 1296000
SBL1, End
|
UEFI Start
RAM Entry 0 : Base 0x0000000080000000
Load CPU 0 Slp: 0x82, Int: 0x10
Memory Base Address: 0x80000000
UEFI End
|
kernel

---
Creating uboot images in android
Toolchain and uboot tools
export ARCH=arm
export PATH=~/gcc-linaro/bin/:$PATH
export CROSS_COMPILE=arm-linux-gnueabihf-
sudo apt-get install u-boot-tools
Source code
url = https://source.codeaurora.org/external/imx/uboot-imx
Configuration
make imx7dsabresdandroid_defconfig
Build
make -j32

---
Creating uboot images in android
*/bin/bash -c "for ubootplat in imx7d:imx7dsabresdandroid_defconfig imx7d-epdc:imx7dsabresdandroid_defconfig; do	UBOOT_PLATFORM=\`echo \$ubootplat | cut -d':' -f1\`;	UBOOT_CONFIG=\`echo \$ubootplat | cut -d':' -f2\`;	make -j2 -C device/imx7/uboot/ CROSS_COMPILE=\" /home/krishna/AOSP_P_IMX_PORT/my_IMX/prebuilts/gcc/linux-x86/arm/arm-linux-androideabi-4.9/bin/arm-linux-androidkernel-\" distclean;
u-boot.imx is the final image for uboot (for sdcard flashing)
u-boot.bin is a raw binary image
u-boot is an image in ELF binary format

---
Uboot directories
arch/
board/
configs/
drivers/
include/
etc...

---
Boot loader flow
* Execution typically starts with an architecture-specific (and possibly CPU- specific) start.S file.
Ex: arch/arm/cpu/armv7/start.S
- before executing this start.S, ROM would be initialized.
- Rom initialization done by POST.
- start.S will set up the SDRAM and serial UART.
- lowlevel_init(), board_init_f(), board_init_r() these are some essential function calls in start.S

---
Boot loader flow
* Configurations
- Configuration depends on the combination of board and CPU type; all
such information is kept in a configuration file
"include/configs/mx7dsabresdandroid.h"
- we need to configure below
CPU Type,Board Type,Cache,Serial Ports,Console Baudrate,Kgdb Serial Baudrate,Watchdog,Real-Time Clock,GPIO,PWM,USB,I2C,SPI etc…
Example:
drivers/watchdog/Makefile:16:obj-$(CONFIG_AT91SAM9_WATCHDOG) += imx_watchdog.o

---
ANDROID OS with bootloader
applications
 Framework
 HAL
 Kernel mode
 UEFI
 SBL
 PBL
 Hardware

---
Conclusion
POST : Supplies the power to circuitry in SOC
boot rom : It contains the first code that is executed by processor after POST.
Boot loader: It will loads the os image to working memory.
UEFI : Mediator between bootloader and kernel mode
Kernel : It will search for the init in the system files and launch the root	process
init : amount the directories and and run the init.rc file for the services