Bootloader :

Bootloader is a piece of code that runs before any operating system is running. ... Bootloaders usually contain several ways to boot the OS kernel and also contain commands for debugging and/or modifying the kernel environment.

All systems need a bootloader
This bootloader is Responsible for:
Early hardware initialisation
Load and boot kernel and initial ram filesystem
System maintenance, including loading and flashing new kernel and system images

Examples :
Uboot and lk LILO(LInux LOader) GRUB (GRand Unified Bootloader), etc...

Uboot

Das U-Boot is an open-source, primary boot loader used in embedded devices to package the instructions to boot the device's operating system kernel. It is available for a number of computer architectures, including 68k, ARM, Blackfin, MicroBlaze, MIPS, Nios, SuperH, PPC, RISC-V and x86.

From logs below is the first log

U-Boot SPL 2018.03-dirty (Sep 24 2019 - 19:49:26 +0530)
this message is from SPL

SPL:
The U-Boot Secondary Program Loader (SPL) is a generic implementation included in the U-Boot code that can be used to replace the Xilinx First Stage Boot Loader.
board/freescale/imx8mq_evk/spl.c
We needto handle ddr/LPDDR in spl.c file

DDR Vs LPDDR

In computing, a computer bus operating with double data rate (DDR) transfers data on both the rising and falling edges of the clock signal. This is also known as double pumped, dual-pumped, and double transition. The term toggle mode is used in the context of NAND flash memory.

Low-Power Double Data Rate Synchronous Dynamic Random Access Memory, commonly abbreviated as Low-Power DDR SDRAM or LPDDR SDRAM, is a type of double data rate synchronous dynamic random-access memory that consumes less power and is targeted for mobile computers. It is also known as Mobile DDR, and abbreviated as mDDR.

We need to write the ddr drivers for specific board (imx8mq)
With the above things we need to configure the ddr later we can jump into actual uboot from spl setup

uboot/board/freescale/imx8mq_evk/imx8mq_evk.c
we take over from spl

uboot/common/board_r.c file will search for mmc boot if not control will move to board/freescale/common/mmc.c file to search image for mmc1 (sdcard).

After enter into the uboot we can stop the booting and can see the console to vrify the uboot stuff

if not uboot will search for the android image file uboot/common/image-android.c to get the kernel base address to load the kernel.

For imx8 the base address
Kernel load addr 0x40480000 size 30837 KiB

after uboot kernel come into the picture.
Its a aprt of OS

user space + kernel space = OS

Whenever a user application calls these system call APIs with appropriate parameters, a software interrupt/exception(SWI) is triggered.
As a result of this SWI, the control of the code execution jumps from the user application to a predefined location in the Interrupt Vector Table [IVT] provided by the OS.
This IVT contains an adress for the SWI exception handler routine, which performs all the necessary steps required to switch the user application to kernel mode and start executing kernel instructions on behalf of user process.
Uboot Porting :

adding new board support into uboot source code:

1)create a board file
board/my_vendor/my_board/my_board.c

#include <...>
DECLARE_GLOBAL_DATA_PTR;
int dram_init(void)
{
gd->ram_size = imx_ddr_size();
return 0;
}
int board_init(void)
{
return 0;
}

2)Create the board Kconfig file
board/my_vendor/my_board/Kconfig
if TARGET_MY_BOARD
config SYS_BOARD
default "my_board"
config SYS_VENDOR
default "my_vendor"
config SYS_CONFIG_NAME
default "my_board"
endif

3)Create the board Makefile
board/my_vendor/my_board/Makefile
obj-y := my_board.o

4)Create the board defconfig

configs/my_board_defconfig
CONFIG_ARM=y
CONFIG_ARCH_MX6=y
CONFIG_TARGET_MY_BOARD=y
CONFIG_MXC_UART=y

5)Create the board header file
include/configs/my_board.h

6) Source board’s Kconfig file

LK bootloader

for qcom Android boot loader is the LK boot loader.
LK performs:
*Hardware initialization: setting up vector table, MMU, cache, initialize peripherals,storage,	USB, crypto, etc.
*Loads boot.img from storage.
*Supports flashing and recovery.

LK call flow

1) The sequence starts with arch/arm/crt0.S: _start.

2) The function calls from kmain()

this function contains multiple function calls
thread_init_early()
arch_early_init()
platform_early_init()
target_early_init()

bootstrap2()
Alternatively referred to as bootstrapping, bootloader, or boot program, a	bootstrap loader is a program that resides in the computer's EPROM, ROM, or another non-	volatile memory. ... When the computer is turned on or restarted, the bootstrap loader first	performs the power-on self-test, also known as POST.

3) Calls made from bootstrap2()
a. arch/arm/arch.c –arch_init()
this is the first function called for initialization
b. platform/<platform>/(platform.c) –platform_init()
it contains defualt mmu section tables and allocate the memory for this platform

c. target/<target>/(init.c) –target_init()
Init SPMI
Init keypad
Set drive strength and pull configs for SDC pins (we have transitioned to SDHCI)
Init the SD host controller/MMC card; identify the MMC card; set the clock, etc.

d. app/init.c –apps_init()
Init apps that are defined using APP_START and APP_END macros; aboot_init()is
        called
Run the app in a separate thread if it has .entry section

e. app/aboot/aboot.c –aboot_init()
Performs any one of the following operations based on settings/circumstances:
Regular boot
Fastboot mode to accept images
Recovery mode to jump to recovery firmware

LK Regular boot:
Pulls out boot.img from the MMC and loads it into the scratch region (base address =
0x80000000) specified in target/msm8916/rules.mk.

BASE_ADDR := 0x80000000
Loads kernel from the scratch region into KERNEL_ADDR (retrieved from boot image
header).
KERNEL_ADDR := BASE_ADDR+0x00800000

LK fastboot mode

*aboot_init checks if:
boot.img not present, or
volume down key is pressed
* Checks reason for reboot – check_reboot_mode.
* Registers handlers for fastbootcommands:
fastboot_register(cmd_list[i].name,cmd_list[i].cb);
*Initializes fastboot
fastboot_init(void *base, unsigned size)
Creates a thread associated with fastboot_handler()
Thread waits for USB event

Fastboot commands
bootable/bootloader/lk/app/aboot/aboot.c

/* register commands and variables for fastboot */
void aboot_fastboot_register_commands(void){
{“flash:”, cmd_flash},
{“erase:”, cmd_erase},
{“boot”, cmd_boot},
etc...
....
....
}

LK recovery mode

aboot_init checks if KEY_HOME or VOLUME UP is pressed.
Checks reason for reboot – check_reboot_mode().
If value at restart reason address is RECOVERY_MODE, sets boot_into_recovery = 1.

boot_linux_from_mmc checks:
if (!boot_into_recovery) {
.........
...
else {
index = partition_get_index(“recovery”);
ptn = partition_get_offset(index);
...........
......
}

Gets image from recovery partition.

gned int target_freq, unsigned int relation);