# I2C Architecture
Introduction:

- I2C is a peripheral bus proposed by phillips.
- I2C intended to allow multiple slaves communicate with one or more masters.
- I2C is only for shorter distance.
- I2C required two signal wires(SDA, SCL).
- The master is always drives the SCL and slaves are the devices responds to the master.
- Both master and slave can share the data over i2c bus but always controlled by master means slaves nerver initiates the transfer.
I2C protocol:
- In i2c data transfered in messages.
- Message contains start/sop condition, address frame, multiple data frames, read/write bit, ACK/NACK bit for each data frame.

- Start Condition:The SDA line switches from a high voltage level to a low voltage level before the SCL line switches from high to low. Stop Condition:The SDA line switches from a low voltage level to a high voltage level after the SCL line switches from low to high.

- Address Frame:A 7 or 10 bit sequence unique to each slave that identifies the slave when the master wants to talk to it.
- Read/Write Bit:A single bit specifying whether the master is sending data to the slave (low voltage level) or requesting data from it (high voltage level).
- ACK/NACK Bit:Each frame in a message is followed by an acknowledge/no-acknowledge bit. If an address frame or data frame was successfully received, an ACK bit is returned to the sender from the receiving device.

How data transfering:
1. data transfered in sequence of 8 bits and these bits placed on the SDA line starting with MSB.
2. SCL line will take 9 pulses (8 pulses for 8 bit data 1 pulse for ACK/NACK bit)
3. If receiving device sends back the low ACK back, its ready to accept another 8 bits of data
  if receiving device sends back the high ACK back, it can accept any data
4. and master will terminate by transfering sop sequence.

##### Write to slave:
1. The first thing that will happen is that the master will send out a start sequence, This will allert all the slaves in the bus
2. master will send the device address,the slave which matches with the address will continue with the transaction
3. slave will decide that the read/write.(0 for write , 1 for read)
4. Master will send data bytes it can continue the sending data (slave will automatically increment internal registers after each byte received.)
5. finally master will send the stop sequence.
Read from slave:
1. This is a little more complicated - but not too much more. Before reading data from the slave device, master must tell it which of its internal addresses it want to read. So a read of the slave actually starts off by writing to it.
2. Same as when master want to write to it: send the start sequence, the I2C address of the slave with the R/W bit low (even address) and the internal register number you want to write to.
3. Now send another start sequence (sometimes called a restart) and the I2C address again - this time with the read bit set. Then read as many data bytes as master wish and terminate the transaction with a stop sequence.